## Slide 1: Time-Series Forecasting Challenge
Tesla Energy Optimization Team
Predicting energy intensity of frequency regulation services in Australia’s electricity market.
November 2018

## Slide 2: Problem Background
The provision of frequency regulation capacity is a critical value stream for monetizing energy storage in wholesale markets today.
  Frequency regulation service is the commitment to provide short-term flexibility in a resource’s power output to maintain grid frequency within nominal ranges.
Frequency regulation capacity is divided into two types of service: raise and lower.
  Frequency Regulation Raise is the provision of capacity for increasing energy discharge (discharge energy to increase frequency.)
  Frequency Regulation Lower is the provision of flexible capacity for increasing energy charge (consume energy to lower frequency.)

## Slide 3: Details Regulation Throughput Ratio
A key economic consideration of frequency regulation for battery storage is the amount of energy conversion associated with a given power market award.
The energy:power ratio of a frequency regulation service is defined as the regulation throughput ratio.
  For a given interval: Regulation Throughput Ratio = Abs[Average power]/Regulation Capacity Award
  For example:
    A resource that averages 5MW (discharging) with a market award of 10MW Regulation Raise would have a 50% Raise Regulation Throughput Ratio. ABS(5MW)/10MW=50%
    A resource that averages -5MW (charging) with a market award of 10MW Regulation Lower would have a 50% Lower Regulation Throughput Ratio.
    ABS(-5MW)/10MW=50%
This ratio has important implications on managing / optimizing the state of charge (SOC) of storage resources in wholesale markets.
    If the throughput ratio is high, then the energy intensity of providing regulation is high.
    If the throughput ratio is low, then the energy intensity of providing regulation is low.
    “Doing nothing” during an interval with a regulation market award equates to a throughput ratio of 0.0
    A traditional “energy” award commands a throughput ratio of 1.0 (i.e. a 10MW energy award results in 10MWh of energy being discharged over an hour).

## Slide 4: Prediction Challenge
Your task is to predict the energy throughput ratio of each frequency regulation (raise and lower) service for each 5-minute interval during October 16-31, 2018.
  For purposes of this exercise, historical regulation throughput ratios (training data) is provided from January 1, 2018 through October 15, 2018.
  The regulation raise and lower throughput ratio values for October 16 – October 31 are left blank and should be predicted from your model.
Notes
  There are no restrictions to how you predict the throughput ratios for October 16-31.
  You can use any of the data that was provided
  Predict the regulation raise and regulation lower values separately. These are different services.
  We are not asking for a prediction on the probability of receiving an award.
    We are asking for your best prediction of what the energy throughput ratio would be in that interval had we received an award.

## Slide 5: Data Sets
frequency.csv (potential feature)
  1-second grid frequency
throughput_ratio.csv (prediction variable)
  average throughput ratio for regulation lower and regulation raise awards for each 5-minute interval
  NaN values indicate no award for the frequency regulation product or there was an award for the opposite product (e.g. the raise regulation throughput ratio will be NaN if there was a lower regulation award in the same interval)
wind_generation.csv (potential feature)
  power reading (MW) at the beginning of each 5-minute interval for 15 wind farms providing power to the grid

## Slide 6: Tasks
Clean and Prepare Data
Analyze Data and Summarize Key Observations
Build Prediction Model

## Slide 7: Task 1 – Clean and Prepare Data
Data Preparation
  Cleaning: eliminate any obvious outlier frequency values (if there are any)
  Transform: convert the 1 second frequency data to four new columns:
    5-minute average values; and
    5-minute median values
    The cumulative sum of 1 second changes in frequency in 5-minute period
    The difference between the initial and last frequency value in 5-minute period

## Slide 8: Task 2 – Analyze Data
Analyze the dataset.
  Summarize any key observations about the data.
  Visualize / plot any key findings where appropriate.
Select a model to generate predictions.
Briefly explain your rationale, quantitatively and qualitatively, for selecting this model type.
  Did you consider any other methods?

## Slide 9: Task 3 – Build Model
Train your model and predict the string of values for both regulation raise and lower throughput ratios for the last two weeks in October.
Provide your forecast values in the blank “?” cells in the CSV
Generate summary visuals of your forecasted values.
List the training features in your model and why those were selected.
Attach a copy of your code
How would you describe the effectiveness of your model?
What additional data would you want?

## Slide 10: Appendix

## Slide 11: Throughput Ratio Illustration
Power
Minute 5
Reg Raise
Power Award
1 second power dispatch
Illustrative 50% Throughput Ratio Interval
Power
Minute 5
Reg Raise
Power Award
Illustrative 10% Throughput Ratio Interval
1 second power dispatch
Minute 0
Minute 0